## Slide 1: aa: magic explained (MEG)
Tibor Auer
MRC Cognition and Brain Sciences Unit Methods group
Notes: Prepare:
/imaging/ta02/Workshop
Wiki

## Slide 2: What you need
Pipelines describing a series of modules to be executed
  <?xml version="1.0" encoding="utf-8"?>
  <aap>
  <tasklist>
  <initialisation>
  <module><name>aamod_checkparameters</name></module>
  <module><name>aamod_evaluatesubjectnames</name></module>
  <module><name>aamod_study_init</name></module>
  <module><name>aamod_newsubj_init</name></module>
  </initialisation>
  <main>
  <module><name>aamod_meg_get_fif</name></module>
  <module><name>aamod_meg_maxfilt</name></module>
  <module><name>aamod_meg_convert</name></module>
  <module><name>aamod_meg_denoise_ICA_1</name></module>
  <module><name>aamod_meg_denoise_ICA_2_applytrajectory</name></module>
  <module><name>aamod_meg_epochs</name></module>
  <module><name>aamod_meg_average</name></module>
  </main>
  </tasklist>
  </aap>
Tasklist

## Slide 3: What you need
Specifies and runs the analysis
  Initialise: setup aa
  Loads in: default parameters and the tasklist
  Customises: parameters and tasks
  Specifies: data and model
  Runs and cleans up: the main (p)art
  Generates: report
User Master Script (UMS)

## Slide 4: What you need
Specifies and runs the analysis
  Initialise: setup aa
    % Automatic analysis
    % User master script example (aa version 5.*.*) - c.a. 1.5h
    %
    % Tibor Auer, MRC-CBSU
    % 01-02-2016
    clear
    aa_ver5
User Master Script (UMS)

## Slide 5: What you need
Specifies and runs the analysis
  Loads in: default parameters and the tasklist
    %% DEFINE SPECIFIC PARAMETERS
    % Default recipe with model
    aap = aarecipe('aap_parameters_defaults_CBSU.xml','/imaging/xy01/Workshop/Material/4_aa/meg_takslist.xml');
User Master Script (UMS)

## Slide 6: What you need
Specifies and runs the analysis
  Customises: parameters and tasks
    % Modify standard recipe module selection here if you'd like
    aap.options.wheretoprocess = 'qsub'; % queuing system % OPTIONS: 'localsingle'|'qsub' for aa engine, typical value 'qsub'
    aap.options.email = 'xy01@mrc-cbu.cam.ac.uk';
    aap.tasksettings.aamod_meg_maxfilt.downsampling = 10;
    aap.tasksettings.aamod_meg_denoise_ICA_2_applytrajectory.toremove = 'spat';
    aap.tasksettings.aamod_meg_epochs.timewindow = [-2000 500];
User Master Script (UMS)

## Slide 7: What you need
Specifies and runs the analysis
  Specifies: data
    % Directory & sub-directory for analysed data:
    aap.acq_details.root = '/imaging/xy01/Workshop';
    aap.directory_conventions.analysisid = 'aa_MEG';
    % Add extra files
    aap = aas_addinitialstream(aap,'channellabels',{'/imaging/rh01/VectorView_MAG_GRD_EEG_EOG_STI101.mat'});
    aap = aas_addinitialstream(aap,'topography',{'/imaging/rh01/Methods/MEGEEGArtifactTemplateTopographies.mat'});
    % Directory for raw data:
    aap.directory_conventions.rawmegdatadir = '/megdata/cbu/ftd';
    aap.directory_conventions.subject_directory_format = 3;
    % Add subject (full):
    aap = aas_addsession(aap,‘run1');
    aap = aas_addsubject(aap,'S1', {[12 442] []},'functional',{'psp_button_press_self_raw.fif'});
    aap = aas_addsubject(aap,'S2', {[13 133] []},'functional',{'ftd_0133_bsp_raw.fif'});
User Master Script (UMS)

## Slide 8: What you need
Specifies and runs the analysis
  Specifies: model
    % Add conditions
    aap = aas_add_meg_event(aap,'aamod_meg_epochs','S1','run1','BP',{'STI101_down' 8192},34);
    aap = aas_add_meg_event(aap,'aamod_meg_epochs','S2','run1','BP',{'STI101_down' 22},34);
User Master Script (UMS)

## Slide 9: What you need
Specifies and runs the analysis
  Runs and cleans up: the main (p)art
    aa_doprocessing(aap);
User Master Script (UMS)

## Slide 10: What you need
Specifies and runs the analysis
  Generates: report
    aa_report(fullfile(aas_getstudypath(aap),aap.directory_conventions.analysisid));
User Master Script (UMS)

## Slide 11: Info/Support
GitHub: https://github.com/rhodricusack/automaticanalysis/wiki
Our Wiki: http://imaging.mrc-cbu.cam.ac.uk/imaging/AA
People (“The AA-team”)
courtesy to Jonathan Peelle